# Port of Kalundborg

# Reception and Handling of Waste 2015-2018

The Harbour's Address:	Kalundborg Havn

#### Vestre Havneplads 7

DK - 4400 Kalundborg

Denmark

Tel.:  +45  59 53 40 00

Fax.:  +45 59 53 40 03

E-mail:  info@portofkalundborg.dk

Responsible for Elaboration:	Port of Kalundborg

Responsible for Execution:	Port of Kalundborg

Relevant Legislation:	Act on Protection of The Marine Environment

(Act no. 963 of 03 july 2013)

Ministerial Order on Port Reception Facilities for Ship-generated Waste on Waste Delivery of Ships and on port Waste Reception Plans

(Ministerial Order no. 415 of 10 May 2012)

Brief Description of the Port of Kalundborg:

The Port of Kalundborg is one of the largest Danish ports measured in calls and turnover of goods.

The Port of Kalundborg owns app. 0.8 million m2 of port area and app. 5,000 m of quays with water depths of up to 15 m. The Port’s total territorial waters (docks and channels) constitute 1.5 million m2.

The Port has 4 main areas: West Harbour, East Harbour, South Harbour, and Dock Harbour. The areas hold a.o. a bulk terminal, ferry terminals, and small fishing and yachting harbours

Within the Port area there are app. 60 active leases of app. 450,000 m2 in total. The remaining area is used for roads, railway infrastructure, quay roads, and working areas. There are still leases available for port-using companies.

Areas of Application:

This waste plan applies to all vessels calling at the Port of Kalundborg.

This plan also applies to calls from Danske Faerger A/S.

List of Contents

1.  General Rules on Waste Reception	3

2.  Purpose and description of the Port’s waste reception facilities	4

3.  Types and amount of receivable garbage and possible cargo residues	4

4.  Information on placement of the reception facilities	4

5.  Description of the fee scheme	4

6.  Written notification	5

7.  Assessment of the need for changes in the Harbour's reception facilities and capacity	5

8.  Consultation of Port users	6

9.  Reporting by insufficient capacity	6

10.  The coming into force	6

Appendix 1. Map ………………………………………………………………………………………..7

Appendix 2. Definition of waste types, collection and disposal	8

Appendix 3. List of the Port’s waste transportation agents and waste recipients	11

Appendix 4. Notification Formula	12

Appendix 5. Formula for Complaint of Insufficient Harbour Waste Reception Facilities	15

1.  General Rules on Waste Reception

The Port of Kalundborg has established the waste reception facilities in accordance with acts at present in force.

Vessels calling at the Port of Kalundborg are obliged to dispose of their waste before leaving the Harbour, cf. the Ministerial Order of the Danish Ministry of the Environment no. 415 of 10 May 2012.

The following general rules are to be observed:

Time of delivery:

Waste delivery shall take place during the Port’s working hours.

The fixed working hours are Monday through Thursday from 7 AM to 3:30 PM, and Friday from 7 AM to 3 PM.

Ships calling at the Port of Kalundborg outside working hours may deliver waste only if the ship can document that delivery at previous or following harbours within working hours is not possible.

Special conditions prevail - see appendix 2 for each waste type.

# Notification:

Ships planning to call at Port of Kalundborg must no later than 24 hours prior to arriving send a notification of waste delivery. See details in section 6.

# Amounts:

Exempt of fee is only garbage corresponding to the type and size of the ship and in relation to the prior port of call. For most ships this amounts to a 700 litres garbagecontainer. For larger amounts of garbage and cargo residues separate payments according to the tariff will be collected. If there is a need for disposal of amounts larger than fitted to harbour capacity, the Port may grant an exemption, cf. the rules of the Ministerial Order

# Types:

The reception facilities and obligation to deliver for each type of waste are stated in appendix 2. Oil waste/oil composites of any kind containing petrochemicals, products of toxicity class I & II, or emulsifying substances are not received. Companies who ship or receive fluids in bulk, and companies who repair ships, shall receive fluid ballasting and tank washing fluids themselves, and they must ensure and defray the expenses of delivery of these fluids to a treatment facility approved by the Authorities.

# Property Right:

The property right to the garbage is transferred to Port of Kalundborg, when the waste is accepted and received at the approved reception facility.

# Responsibility:

The ship-owner vouch for the correctness of all information given by the shipmaster on the waste in terms of type, composition, amounts, time of collection, and damages caused by errors or defects, including during servicing.

Thus the ship-owner is responsible for any damage resulting from incorrect, misleading, or insufficient information provided by the shipmaster. This also applies to damages inflicted upon a third party as a result of incorrect, misleading, or insufficient information provided by the shipmaster.

According to current Ministerial Order, ships eg. omitting to deliver waste in accordance with the regulations of the Ministerial Order, or omitting to observe the demand for notification, will be imposed a fine. If the actions are negligent, the punishment may even be mitigated imprisonment or up to 2 years imprisonment. Delays and loss of time due to waste delivery are irrelevant to the Port of Kalundborg.

For further information please contact Port of Kalundborg:

Tel: +(45) 59 53 40 00,  Fax.:  +(45) 59 53 40 03,  E-mail:  info@portofkalundborg.dk

Reception of waste is administered by the operations department at Port of Kalundborg.

2.  Purpose and description of the Port’s waste reception facilities

By the establishment of effective reception facilities Port of Kalundborg wishes to contribute to a positive effect on the environment by responsible handling of the ships' garbage and cargo residues.

The aim is to provide a smooth delivery of waste from ships calling on Danish harbours - and thereby contribute to the reduction of marine pollution.

Each shipmaster is kindly requested to familiarise himself with the working hours and the level of service at the reception facility as well as identifying the responsible person.

Furthermore, each shipmaster is requested to divide his waste into fractions fitting into the sorting system chosen by Port of Kalundborg, see the table in appendix 2 for further information. The table is based on the MARPOL fractions.

3.  Types and amount of receivable garbage and possible cargo residues

The amounts of waste delivered at Port of Kalundborg from 01.01.2013 to 31.12.2013  were composed as follows:

- 93,7 tons of garbage (refuse / galley waste)

- 247 tons of slop oil

- 215 m3 of sewage wastewater (black water)

The amounts of garbage are stated by the recipient.

The Port of Kalundborg requests the waste recipients send an annual account of waste amounts, and the Port will actively work at making the ships fill in the Notification Formula (appendix 4) before arrival.

4.  Information on placement of the reception facilities

The Port of Kalundborg uses mobile devices, except for ferries.

A series of waste containers for the ships' garbage and galley waste are placed on the Harbour area. Containers for oil waste, etc. are placed at the fishing harbour and yachting harbour. The location of the permanent reception facilities is marked on the outline map of the Harbour area in Appendix 1.

5.  Description of the fee scheme

The fee for delivery of garbage is guided by the ”No-Special-Fee” principle (NSF), which means that all expenses for waste disposal and expenses for establishment and operation of the reception facilities are included in the usual harbour charges.

However, separate payment is collected if one or more of the following points are valid:

- The amount of waste to be delivered is larger than the amount of waste the ship - considering its type and size - would usually generate since its previous harbour call. Normally max. 700 litres.

- The waste is delivered outside working hours.

- The ship does not pay harbour charges.

- The ship omits to notify the Harbour within 24 hours of its disposal needs. This rule does not apply if the ship can present documentation of the the fact that observation of the 24-hour notification has not been possible.

All cargo waste (cargo residues) are subject to separate payment.

The fee for delivery of other types of waste appears in appendix 2, where possible fees are stated for each of the major MARPOL waste types.

The Port’s expenses connected to handling of waste appears in the Annual Accounts of the Port.

6.  Written notification

Shipmasters planning to call at Port of Kalundborg must within 24 hours prior to arrival submit a written notification to the Harbour. The notification may be send by the ship's local agent. The demand for notification applies to all ships with the exception of ferries, towboats, pilot boat, fishing boats, and pleasure crafts.

A notification formula is attached in appendix 4. The notification formula may be obtained in Danish and English at the Harbour Master's Office, or can be found on the port’s homepage or at the homepage of the Danish EPA (www.portofkalundborg.dk  or  www.mst.dk ).

The formula is to be sent or faxed +(45) 59 53 40 03, or e-mailed: info@portofkalundborg.dk

7.  Assessment of the need for changes in the Harbour's reception facilities and capacity

The Port of Kalundborg continuously assesses the existing facilities for reception of the various types of waste, and adapts the capacity to the current conditions to obtain sufficient capacity. Reports from users on insufficient capacity are continuously treated by the Harbour to assure sufficient capacity.

Environmental Garbage

Envitonmental garbage (oilpoluted rags, oilfilters, batteries, cemicals etc.) is gathered in a container. This is emptied once every month. The garbage is collected by the the local authorities environmental department.

Sewage:

The Port of Kalundborg uses a mobile unit (mud pump) called in from the city's sewage disposal plant, except for the ferry port where pipelines are connected to the public sewer.

Fishing boats and pleasure crafts may dispose of wastewater from chemical toilets in the harbour toilets facilities.

Furthermore, pleasure crafts are referred to the nearby yachting harbour where they will find a permanent installation for emptying of holding tanks and chemical toilets.

Slop oil and other types of waste oil:

The Port of Kalundborg uses a mobile unit (tanker) from Dansk Olie Genbrug A/S (DOG) in Kalundborg. Fishing boats and pleasure crafts may dispose of waste oil in the oil drums placed under the shed roof at the fishing harbour. Three sets of waste containers with drums for waste oil, paint residues/chemicals and residual waste are placed in connection with the winter berths for pleasure crafts.

Garbage (refuse / galley waste):

The ferry to Samsø dispose all of their garbage at Samsø, so it has an exception to deliver garbage in Kalundborg. The pilot boat, fishing boats and pleasure crafts may use the containers placed within the harbour area, including the municipal bottle containers places at the fishing harbour.

Other ships may requisition separate containers for disposal of garbage through the Harbour Master's Office

Garbage from cargo vessels calling at the Harbour is not currently sorted, but is disposed unsorted into the container, after which it is brought to incineration. Accumulators, iron and chemicals are to be placed at the quay next to the container.

Updating:

Every three years a thorough revision of the total waste plan is carried out in preparation for necessary alterations.

8.  Consultation of Port users

Wen necessesary the Port of Kalundborg summons a number of frequent harbour users to discuss the efficiency of the reception facilities.

9.  Reporting by insufficient capacity

Reporting in case of insufficient waste recipient capacity should be made to the Harbour Master's Office, see appendix 5, Formula for Complaint. The complaint is to be sent to the Port, who in turn will then send a copy to the Danish EPA.

10.  The coming into force

These regulations will come into force on the 16. of December 2014  substituting regulations previously disseminated.

Date 27 of December 2014

Signature

Jakob Beck Jensen                                     	Bent Rasmussen

Chairman of the Harbour Board	Port Director

Slipway / hauling                         Winther berths for yatchs              Containers for garbage (galley waste)                  Drums for waste oil	       Appendix 1

Appendix 2. Definition of waste types, collection and disposal

| Waste Type | Collection | Disposal | Fee |
| --- | --- | --- | --- |
| MARPOL annex 1 Oil and chemical waste All types of waste stemming from transportation of oil, such as fuel, machine slop, tank washing water, and dirty ballast water. | Enquiries should be made to the Port of Kalundborg with binding notification no later than 24 hours before collection. An order is made by sending a letter of notification to fax. +(45) 59 53 40 03 or via e-mail: info@portofkalundborg.dk Machine slop, tank washing water and dirty ballast water is collected in tanker/mud pump, and is then delivered to an approved recipient. By smaller amounts (< 1 cbm) drums filled by the ship itself are delivered/collected. | The ordered tanker/mud pump is responsible for the disposal. Machine slop and other waste oil/oily water is delivered to Dansk Olie Genbrug (DOG) in Kalundborg for processing. | Machine slop and chemical waste from operations in amounts expected considering the ship's type, size, and speed from the previous Harbour are collected free of charge. Machine slop etc. must be pumped on shore by use of the ship’s own pumps with a capacity of minimum 2 m3/hour. In other cases, or if waste is delivered outside working hours, a fee is due at the current rate. |

| Waste type | Collection | Disposal | Fee |
| --- | --- | --- | --- |
| MARPOL annex II and III Cargo waste Liquids carried in bulk. Harmful substances carried in packaged form. | This waste falls into the category of special waste and is not received at the Port of Kalundborg. This type of waste must be delivered at a cargo recipient or shipper in accordance with agreement made with the ship's agent or shipper. The waste must be packed and declared in compliance with the current IMO stipulations. Waste sorting at source must take place. | Approved recipients. | The cost is a concern between the ship and its agent who settles directly with the shipper/recipient. Alternatively, the Port of Kalundborg may assist with the organisation and collect the actual costs with the addition of an administration fee. |
| MARPOL annex IV Sewage from ships Sewage and other waste deriving from toilets, lavatory basins, baths, drains placed in hospital rooms, and other places with living animals or other types of wastewater mixed with the named substances. (Grey water and black water) | Enquiries should be made to the Port of Kalundborg with binding notification no later than 24 hours before collection. An order is made by sending a letter of notification to fax. +(45) 59 53 40 03 or via e-mail: info@portofkalundborg.dk Sewage is collected in tanker / mud pump. In the ferry port pipelines are connected to the public sewer. | The sewage collected by tanker / mud pump is delivered to the municipal disposal plant. | Sewage is collected by tanker / mud pump free of charge in amounts expected considering the ship's type, size, and speed from the previous Harbour are collected free of charge. In other cases, or if waste is delivered outside working hours, a fee is due at the current rate. For passenger ships (ferries) and cruise lines special agreements are in force. Sewage must be pumped on shore by use of the ship’s own pumps with a capacity of minimum 2 m3/hour. If this is not observed, an additional fee is incurred by the hour. For passenger ships (ferries) and cruise ships separate conditions apply. |

| Waste Type | Collection | Disposal | Fee |
| --- | --- | --- | --- |
| MARPOL annex V Garbage from ships Garbage produced as a natural part of the ship's daily operations. Chemical residues and other dangerous substances may not be dumped in the waste containers. | A series of waste containers for the ships' garbage are placed on the Harbour area. They are accessible at all hours. The location of the permanent containers is marked on the outline map of the Harbour area in Appendix 1. The containers are emptied in fixed intervals within the Harbour's working hours. Extra containers may be ordered. Enquiries should be made to the Port of Kalundborg with binding notification no later than 24 hours before required delivery. An order is made by sending a letter of notification to fax. +(45) 59 53 40 03 or via e-mail: info@portofkalundborg.dk Metals and scrap is to be placed on the quay for collection by harbour staff. Chemical waste must be responsibly packaged and its contents be clearly marked. | The content of these containers is sent directly to incineration in accordance with current regulations. Chemical waste is delivered to Kommunekemi through the municipal collection unit. | The fee for delivery of garbage in the permanent or ordered containers is guided by the ”No-Special-Fee” principle (NSF), if the amounts are expected considering the ship's type, size, and speed from the previous Harbour. In other cases, or if containers are ordered outside working hours, a fee is due at the current rate. For passenger ships (ferries) and cruise ships separate conditions apply. |

Appendix 3. List of the Port’s waste transportation agents and waste recipients

List of Harbour's Waste Transporters and Waste Collectors

| The Port of Kalundborg only uses approved waste disposers as subcontractors |
| --- |
| Sewage wastewater | Kalundborg Sewage treatment plant, tel: +45 59 53 40 45 |
| Machine slop and other waste oil | Avista Oil A/S, Juelsmindevej 18, 4400 Kalundborg tel: +45 59 56 56 44 |
| Garbage (galley waste) | Axel Hansen / Sophienlundsvej 8, 4300 Holbæk. Tlf: 59 43 30 99 - and local collectors/carriers by need for extra containers |
| Iron and scrap | Vestsjællands Jernhandel Jorløsevej 33, 4470 Svebølle Tel: +45 59 29 36 81 |
| Chemical waste | Kalundborg Brand og Rednings Miljøafd. Tel: +45 59 53 40 24 |

Appendix 4. Notification Formula

Appendix 5. Formula for Complaint of Insufficient Harbour Waste Reception Facilities

To:

Port of Kalundborg

Vestre Havneplads 7

DK - 4400 Kalundborg

Complaint of insufficient waste reception facilities:

Suggestions for improvement:

Remarks, if any:

Sincerely

|  | Please contact me for elaboration of the above by |
| --- | --- |
| phone: |  |
| or |  |
| email: |  |

The Port of Kalundborg will send a copy of this complaint to the Danish Environmental Protection Agency